## Slide 1: MCUNet Tiny Deep Learning on MCUs
23/06/2026
Enoch Richbert J

## Slide 2: Agenda
The Promise
  What can MCUNet do?
The Process
  How does MCUNet work?
    Techniques that reduce peak SRAM
    Techniques that reduce latency
The Playbook
  How to integrate this into our MCU project?
The Possibilities
  What next?

## Slide 3: The Promise

## Slide 5: The Process
System-Algorithm Co-design

## Slide 6: The Process
Peak SRAM Reduction
  Patch-based inference
  Global memory scheduling
  In-place depthwise convolution
  Static buffer placement
Latency Reduction
  No interpreter
  Specialized per-shape kernels
  Cache friendly data layout
  Loop optimizations

## Slide 7: Peak SRAM Reduction

## Slide 8: Patch-based inference
Imbalanced Memory Distribution of CNNs (MobileNetV2)

## Slide 9: Patch-based inference
Notes: Input image = 64 × 64 × 3 Conv1: 3×3 kernel
stride = 1
output channels = 16
64 × 64 × 16 = 65,536 bytes (if int8) ≈ 64 KB
+----+----+ | P1 | P2 | +----+----+ | P3 | P4 | +----+----+ 32 × 32 × 16 16 KB

## Slide 10: Global memory scheduling
One static arena with compile-time offsets
Dead-tensor byte reuse via lifetime analysis
Zero runtime cost, large peak-SRAM reduction

## Slide 11: Global memory scheduling

## Slide 12: In-place depthwise convolution
Depthwise conv whose output buffer is its input buffer
  Input tensor is overwritten as the layer runs
No extra compute, no accuracy change, just a different addressing pattern.

## Slide 13: In-place depthwise convolution

## Slide 14: In-place depthwise convolution
Each of the 18 depthwise kernels is specially written so in-place computation can be done without write-back hazards.

## Slide 15: Latency Reduction
NHWC and NCHW
Use NHWC for Point-wise Convolution
  For each pixel, all channels are stored contiguously, then move to the next pixel.
Use NCHW for Depth-wise Convolution
  Store all of channel 0's pixels, then all of channel 1's pixels, then channel 2's

## Slide 16: Latency Reduction
Loop optimization
Loop reordering
  Optimizes locality by reordering the sequence of loops.
Compile-time loop bounds
  Loop count is a constant stored in a register. Helps skip runtime bounds checks
Loop unrolling
  Reduces branching overhead at the expense of its binary size.

## Slide 17: Latency Reduction
Layer Fusion
Conv + BN + Activation + Requant all baked into one call
BN is fused at compile time
Requant + activation are fused into the inner loop of specialized kernel
Notes: BN is learned standardization step inserted between layers..
Without fusion (e.g. naive TFLite Micro), the path looks like:
[input tensor] → Conv → [int32 tensor in DRAM]
→ Requant → [int8 tensor in DRAM]
→ BN → [int8 tensor in DRAM]
→ ReLU → [int8 tensor in DRAM]
↑ next layer reads this
Four passes over the data, four temporary buffers, four kernel dispatches.
With fusion (your code):
┌──────────────── one kernel ───────────────┐
[input] → MAC accumulate → ×scale → +offset → clamp → write int8 → next layer
(conv) (requant fused) (act fused)
BN folded into weights at codegen

## Slide 18: The Playbook

## Slide 19: The Possibilities
On-Device Training
Object Detection
Temporal Shift Modules for complex gesture control

## Slide 20
Thank You!