## Slide 1
TinyEngine: High-Performance Inference for Resource-Constrained MCUs
• From TFLM Runtime to System–Algorithm Co-Design
• Presenter: Embedded-ML Staff Engineer
• Target: Engineers already shipping with TFLM
• Focus: Generated code vs. interpreted graphs

## Slide 2
The MCU Envelope
• SRAM: 128 KB – 1 MB
• Flash: 512 KB – 4 MB
• Cortex-M4/M7: 100 – 600 MHz
• Power: Single-digit mW budgets
• SRAM is the binding constraint for vision

## Slide 3
Why Activations Break the Budget
• Weights live in Flash (cheap/abundant)
• Activations live in SRAM (scarce/expensive)
• Example: 160x160x16 int8 feature map
• 160 * 160 * 16 = 409,600 bytes
• Fails on a 256 KB SRAM part immediately

## Slide 4
TFLM at a Glance
• Model (.tflite) -> MicroInterpreter <--- AllOpsResolver
• Tensor Arena (Greedy Workspace) -> CMSIS-NN / Kernels
• Portable and generic architecture
• Single binary covers many models
• Flexible deployment model

## Slide 5
Where TFLM Leaves Performance on the Table
• Per-invocation operator dispatch overhead
• Greedy arena allocator lacks future visibility
• Generic kernels branch on shape/stride at runtime
• Interpreter and resolver tables consume Flash
• Trade-off: Flexibility vs. Efficiency

## Slide 6
MCUNet in One Picture
• Automated Search + Specialized Runtime
• TinyNAS finds the network architecture
• TinyEngine executes that specific architecture
• Co-design loop prevents un-deployable models

## Slide 7
Code-generation, Not Interpretation
• Ingests Quantized TFLite and emits straight-line C code
• No interpreter, no resolver machinery
• No FlatBuffer parsing at runtime
• The "engine" is the generator script; what runs on target is pure C

## Slide 8
Codegen Pipeline
• TFLite Model -> [Graph Analyzer] --- Lifetime Birth/Death
• [Memory Scheduler] - Buffer Packing
• [Op Generator] ----- Specialized C
• Output: Emitted C + Weights + Headers

## Slide 9
What the Graph Analyzer Sees
• Exact tensor shapes and types
• Precise birth/death op indices
• Inter-op dependency chains
• Full-graph visibility vs. TFLM's greedy/local view

## Slide 10
What the Operator Generator Emits
• Specific kernel implementation per layer
• Example: depthwise_kernel3x3_stride1_inplace.c
• Compile-time specialization eliminates runtime parameter branching
• Constants are inlined directly into the kernel source

## Slide 11
Side-by-Side Execution
• TFLM: Model -> Interpreter -> Op Resolver -> Generic Kernels
• TinyEngine: Model -> Generated invoke() -> Specialized Kernels
• Eliminates runtime dispatch layers entirely

## Slide 12
What This Buys and Costs
• Buys: Lower latency, smaller SRAM, cross-op optimization
• Buys: Smaller Flash for the "runtime" logic
• Costs: Re-codegen/re-flash required to change models
• Costs: No dynamic model loading at runtime
• A deliberate trade for absolute performance

## Slide 13
Global Memory Scheduling
• Uses full-graph lifetime knowledge to pack activations like registers
• Tensors with non-overlapping lifetimes share physical storage
• 50–70% peak-SRAM reduction vs. TFLM on identical graphs
• T1: [=====] | T2: [===] | T3: [=====] (T1 and T3 reuse buffer)

## Slide 14
In-place Depthwise Convolution
• DW 3x3 Stride 1 calculations are locally bounded
• Reads small neighborhood and writes back to input buffer directly
• Saves one full activation tensor per layer
• Crucial for MobileNet-class networks (_inplace_CHW_fpreq.c)

## Slide 15
Patch-based Inference
• Breaks large inputs into spatial patches
• Runs patch through several layers top-to-bottom
• Only materializes small patch activations at any one time
• Enables 320x320 inputs on small MCUs
• Trade-off: Slight recomputation at patch boundaries

## Slide 16
Layer Fusion
• Conv + BN + ReLU + Add collapsed into a single kernel pass
• Minimizes intermediate memory traffic to SRAM
• Fuses pre-quantization sequence that compiler constant-folds
• Improves instruction cache footprint

## Slide 17
Static Scheduling and Specialized Kernels
• No virtual dispatch or runtime function pointers
• Compiler sees concrete loop bounds for optimized unrolling
• Zero runtime shape or stride checks in the execution loop
• Cleanly optimized for CMSIS-NN primitives at compile time

## Slide 18
Quantization Plumbing
• int8 weights with per-channel scales
• int8 activations with per-tensor scales
• Fixed-point requantization (_fpreq) natively handled
• Constants are inlined at codegen time, eliminating table lookups

## Slide 19
A 4-layer Toy Graph Scenario
• Conv1(T1) -> DWConv2(T2) -> PWConv3(T3) -> Conv4(T4)
• T1 size: 32 KB, Born L1, Dies L2
• T2 size: 32 KB, Born L2, Dies L3
• T3 size: 16 KB, Born L3, Dies L4
• T4 size: 8 KB, Born L4, Dies end

## Slide 20
Greedy vs. Global Allocation
• Greedy Max Live: T1 + T2 = 64 KB total allocation required
• Global Allocation: Reuses T1's storage slot for T3
• Peak SRAM drops from 64 KB down to 40 KB
• 37% memory saving on toy example without accuracy loss

## Slide 21
What the Generator Drops on Disk
• genModel.h: Defines PEAK_MEM, MODEL_SIZE, weight declarations
• genModel.c: invoke() sequence containing straight-line layer calls
• weights.c: const int8_t arrays placed cleanly in flash
• Specialized kernel files: convolve_*.c, depthwise_*.c

## Slide 22
invoke() in Practice
• void invoke(void) { layer1_conv2d(); layer2_dw_inplace(); ... }
• No loops, dispatch tables, or string lookups
• Fully unrolled execution graph
• Enables superior static analysis / WCET behavior

## Slide 23
Mapping Layers to Memory
• Weights -> Flash (.rodata / external QSPI if required)
• Activations -> SRAM / DTCM for optimal throughput
• Input/Output buffers mapped to reuse activation arena boundaries
• DTCM placement provides massive latency wins on Cortex-M7

## Slide 24
End-to-end Pipeline
• Train (PyTorch/TF) -> Post-Training Quantization -> .tflite
• TinyEngine Codegen converts TFLite to localized C sources
• Embedded Toolchain compiles C sources natively to Flash target
• Divergence happens entirely at the runtime boundary

## Slide 25
What You Actually Link In
• Generated genModel.c and weights.c files
• Only the kernel subset explicitly required by your network
• CMSIS-Core / CMSIS-DSP foundational layers
• Zero bloated library overhead or generic unreferenced fallback ops

## Slide 26
Application Integration
• Main execution loop: acquire_frame() -> invoke() -> consume_logits()
• Fully compatible with bare-metal, FreeRTOS, or Zephyr RTOS
• invoke() is a simple, predictable synchronous function call
• Zero dynamic heap requirements

## Slide 27
TFLM vs. TinyEngine, Head-to-Head
• Runtime: Interpreter (TFLM) vs. Generated C (TinyEngine)
• Memory: Greedy local allocation vs. Global full-graph scheduling
• Optimizations: Basic vs. In-place DWConv + Patch-based inference
• Tradeoff: Broad op coverage vs. Absolute minimal memory footprint

## Slide 28
Case Study: VWW0 on PIC32CZ-CA
• Hardware: Microchip PIC32CZ-CA (Cortex-M7) + OV7670 Camera
• Model: MCUNet-VWW0 (Person / No-Person binary classifier)
• Input Profile: 64x64x3 int8 quantized stream
• Structure: 51 layers containing 18 in-place depthwise variants

## Slide 29
Results: VWW0 + TinyEngine Production Gains
• Peak SRAM Activations: Dropped from 257,448 B down to 60,800 B (-76%)
• Flash Weights: Increased from 190,864 B to 399,656 B (+109%)
• Inference Latency: Accelerated from ~330 ms down to <70 ms
• Successfully traded abundant Flash to resolve binding SRAM constraints

## Slide 30
Honest Tradeoffs & Limitations
• Significantly narrower operator coverage compared to TFLM ecosystem
• Exotic or non-MCUNet topologies may fail code generation
• Model updates require complete re-codegen and firmware re-flash
• Debugging abstract generated kernel variations increases complexity

## Slide 31
Future Directions
• MCUNetV2: Refined patch-based execution and receptive field sharing
• MCUNetV3: On-device ultra-tiny training capabilities
• Sparse updating and localized quantized backpropagation on MCU
• Shift toward pure compilation-based edge runtimes

## Slide 32
Key Takeaways
• TinyEngine is a code generator, not a generic runtime interpreter
• Global memory scheduling delivers the largest share of the SRAM win
• In-place DWConv and layer fusion optimize MobileNet structures
• Patch-based inference opens the door for high-resolution edge vision
• Integration is a lightweight drop-in replacement for the TFLM layer

## Slide 33
Q&A
• Operator coverage & fallback patterns
• Model-swap workflow alternatives
• Debugging generated straight-line code blocks
• Comparisons to ONNX Runtime / Glow / ExecuTorch